## Slide 1: SP Office Gadget: IoT Doorbell
Hackware v3.0 (3 May 2017)
SP Digital Tech Talk (29 Dec 2016)
By: Yeo Kheng Meng (yeokm1@gmail.com)
https://github.com/yeokm1/sp-iot-doorbell

## Slide 2: Problem?
My office needs a doorbell
Solution: An overengineered IoT doorbell

## Slide 3: Solution Outline
Rings when button is pressed
Informs Slack channel via Wifi connection
Takes photo and uploads to Slack
File system resilience against improper shutdown

## Slide 4: Demo video
https://www.youtube.com/watch?v=MGRNmj3iRuI

## Slide 5: MVP Dev Set
Raspberry Pi 3
8MP RPi camera v2
  Sony IMX219
  Connected via Camera Serial Interface connector
3V-20V DC Continuous Buzzer
Wire simulated as a button

## Slide 6: The button

## Slide 7: Camera
5MP 160° Horizontal Wide Angle (Fisheye lens)
  Usual 72°
70cm flex cable
  Usual 10cm
https://www.seeedstudio.com/Raspberry-Pi-Wide-Angle-Camera-Module-p-2774.html

## Slide 8: Raspistill’s camera settings
/opt/vc/bin/raspistill -ISO 800 -ss 40000 -q 50 -rot 270 -t 1 -w 1024 -h 768 -o /tmp/iot-doorbell-visitor.jpg
30% JPEG quality
270° rotation
1 millisecond picture-taking delay
  Default 5 seconds
  0 value does not work
640x480 resolution
-> ~100KB file size
ISO 800
40ms shutter speed

## Slide 9: Slack integration
Create Slack bot and get token
https://sp-digital.slack.com/apps/A0F7YS25R-bots
Post Message API: https://api.slack.com/methods/chat.postMessage
File Upload API: https://api.slack.com/methods/files.upload
Slack Python SDK Bug: Only allows file upload from user, not bot
https://github.com/slackapi/python-slackclient/issues/102

## Slide 10: Operating System
Arch Linux ARM
  My FAVOURITE for personal Raspberry Pi projects
  https://archlinuxarm.org/platforms/armv8/broadcom/raspberry-pi-3
Minimal packages OOTB
  OOTB: Package Manager (pacman), networking, shell, text editor, SSH
  No Git, wget, GUI, Python, GCC
Cutting edge kernel and package releases
  Node.js
  Python3 as default python

## Slide 11: Console access via USB-UART
Access console without SSH
SSH disabled for security
Add to /boot/config.txt
  enable_uart=1
Refer to:
  https://engineers.sg/video/raspberry-pi-3-uart-bluetooth-issues--609
  Hackware (30 March 2016)

## Slide 12: Read-only file system for embedded systems
Prevent file-system corruption during improper shutdown
Increase SD card/flash lifespan

## Slide 13: Read-only file system options
----------------/etc/fstab------------------------
/dev/mmcblk0p1 /boot vfat defaults,ro,errors=remount-ro 0 0
tmpfs /var/tmp tmpfs nodev,nosuid 0 0
tmpfs /var/log tmpfs nodev,nosuid 0 0
------------------------------------------------------
tmpfs: RAM drive used for temp and log directories
----------------/boot/cmdline.txt------------------------
Set “ro” option for root directory
----------------------------------------------------------------
----------------/etc/systemd/journald.conf-----------
Storage=none
----------------------------------------------------------------
https://gist.github.com/yeokm1/8b0ffc03e622ce011010